## Slide 1: Reconstruction of Complex Structures with Online Profiling and Adaptive Viewpoint Sampling Abdullah Abduldayem, Dongming Gan, Lakmal Seneviratne and Tarek Taha

## Slide 2
Khalifa University, Abu Dhabi, UAE

## Slide 3: Motivation
Need to construct fast, inexpensive, high resolution models of large and complex structures (such as aircrafts, bridges etc) for inspect on, MRO etc. using small UAVs.

## Slide 4: Model-based Exploration
If a CAD model is available (e.g. for an aircraft), coverage paths can be computed offline
Challenges:
Aligning model frame with world frame
Uncertainties
Taken from [4]

## Slide 5: Exploration without Models
No prior knowledge of structure
Iterative process - Select next best view that leads to highest coverage
Explore until a termination condition is satisfied

## Slide 6: Specification
Autonomous inspection
No prior knowledge or model of structure
Large complex structures
Fast real-time inspection
Assumptions
Known workspace dimensions (maximum size)
Symmetric shape

## Slide 7: UAV Based Inspection
Multirotor UAVs
  Allows for free motion through 3D space
  Short battery life limits length of mission (10-15 minutes)
Payload | Purpose
LIDAR | Measures long-range information
RGB-D camera | Captures textures and dense points
On-board computing | Processes sensor inputs and creates path

## Slide 8: Object Representation - 1
Point Clouds
Set of points in 3D Cartesian space
Continuous space
+ Preserves arbitrarily small details
+ Can create detailed mesh
- No differentiation between free and unexplored space
Taken from [1]

## Slide 9: Object Representation - 2
Voxel Grid
Regular 3D grid that stores values in each cell
Discretized space
Occupancy Grid
+ Differentiates between free and unexplored space
+ Probabilistic
- Resolution
From [1]

## Slide 10: Proposed Approach
Next Best View (NBV) Strategy using
Profiling
and
(b) Symmetry Properties

## Slide 11: Next Best View (NBV) Strategy
Stop
Yes
No
Profiling
Symmetry Detection
Start
Terminate?
Evaluate Viewpoints
Navigate to best view
Update map
Generate Viewpoints

## Slide 12: Profiling
Before performing NBV, we obtain a fast, approximate (low density of points) profile of the object
Wide-angle long-range sensor (LIDAR) is used
Creates an initial map to guide the NBV process

## Slide 13: Profiling – Bounded Box

## Slide 14: Profiling – Typical Run

## Slide 15: Profiling - Results
Time: 160 sec (2.67 min) flight
Distance: 320 m
Coverage: 62% (res=0.10m)
The profile is low density and tends to show scan lines

## Slide 16: Symmetry
Symmetry is used to predict more accurately the object shape, and fill any gaps missed during profiling.
If the object is symmetric, we can use half of the structure to make predictions about the other half

## Slide 17: Plane of Symmetry
Compute keypoints using 3D variant of SIFT
Compute features for each keypoint
Pair similar points
Fit planes of symmetry between each pair of points
Apply mean shift clustering to find best plane

## Slide 18: Symmetry Detection
Key Point Detection

## Slide 19: Symmetry Detection
Key Point Detection

## Slide 20: Symmetry Detection
Plane Fitting
A plane is fitted between pairs of keypoints that have similar features
The coefficients of the plane are then computed

## Slide 21: Viewpoint Generation – 3D Rays
Rays are cast in the sensor field of view (FoV) (within range and resolution)

## Slide 22: Viewpoint Generation
  Constant Grid Viewpoint Sampling (CGVS)
  Viewpoints sampled discretely around the current pose (yellow arrow)
  Sample in Yaw and (x,y,z) Space
(a) Top View
(b) 3D View

## Slide 23: Utility Function – Shannon Entropy
H - Quantity of information that can be obtained

## Slide 24: Utility Function – Ray Tracing
Virtual rays are cast through the grid, stopping once they reach max range or collide with an occupied cell
Entropy along the ray is computed
Ray Entropy = 0.0
Ray Entropy = 1.4
(Occupied)
(Unknown)
(Free)
Legend

## Slide 25: Utility Function
At each generated viewpoint, compute utility function
Viewpoint with highest entropy (largest information gain) is chosen as the “next best view”
 | Probability of occupancy of cell
 | Total entropy
 | Set of unique voxels in view
 | Total entropy
 | Set of unique voxels in view

## Slide 26: Viewpoint Generation
  Adaptive Grid Viewpoint Sampling (AGVS)
 | Distance between viewpoints
 | Scale factor base
 | Distance between viewpoints
 | Scale factor base

## Slide 27: Viewpoint Generation
Global Entropy Change
If falls below a threshold, increase scale factor
also used to terminate NBV process
Iterations

## Slide 28: TEST RESULTS

## Slide 29: Experiments
Quadcoptor
LIDAR and RGB-D sensors
Structure dimensions:
35 x 30 x 7 m3

## Slide 30: Experiments – Typical Run
20x speed

## Slide 31: Experiments - Trajectory

## Slide 32: Experiments - Results
Simulation is run at 5 different starting points
The average results of the five runs is shown below

## Slide 33: Experiments - Results
Profiling (S2-S5) increases coverage with at least 30% travel distance reduction compared to no profiling (S1)

## Slide 34: Experiments - Results
AGVS (S3, S5) increases coverage at the cost of travel distance compared to CGVS (S2, S4)

## Slide 35: Experiments - Results
Symmetry prediction (S4, S5) increases coverage with reduction in travel distance compared to no prediction (S2, S3)

## Slide 36: Concluding Remarks
Use of profiling stage and exploitation of symmetry
Features of Proposed Algorithm
  Enhance utility function by adding distance and point density metrics
  Improved viewpoint sampling by targeting frontier
  Multiple sensors with overlapping fields of view
Results in higher coverage with shorter travel distance

## Slide 38: Mohamed bin Zayed International Robotics Challenge (MBZIRC) www.mbzirc.com
MBZIRC will be held every two years, with total prizes of USD 5 Million.
Provide a technologically demanding set of challenges in Robotics.
Attract the best international teams

## Slide 39: MBZIRC 2019 - Challenge Definition
Extend MBZIRC 2017 Challenges
Autonomous navigation and mobile manipulations, of small aerial and ground vehicles
3 Individual Challenges and a Grand Challenge
Semi-structured outdoor-indoor environments - App. 90mx70m arena

## Slide 40: MBZIRC 2019 - Challenge Definition
Challenge 1 is based on UAV dynamic aerial tracking and interventions in 3D.
Challenge 2 is based on UAV and UGV picking and placing of objects in an indoor-outdoor environment.
Challenge 3 is based on UGV and UAV mobile manipulations in an urban fire search and rescue scenario.
The Grand Challenge will consist of a triathlon type event, combining Challenges 1, 2 and 3.

## Slide 41: MBZIRC 2019 - Timeline
Call for Intent to Participate - September 2017
Call for Proposals – November 2017
MBZIRC - November 2019

## Slide 42: Prize Money Allocation Model
MBZIRC 2019
Team Sponsorship US$ 3 million
Prizes US$ 2 million

## Slide 43: Thank you